Useful formulae: [Note that you may not need all of these formulae. Use as needed]

Utilization:

- , S=2x108m/s

- For stop-and-wait: , where p is the probability that a frame is in error.

Utilization for sliding-window mechanisms with window of w:

- Go back N: , if w fills the pipe, or otherwise

- Selective repeat: , if w fills the pipe, or otherwise

- M/D/1: queuing delay ; Ts is service time & ( is link utilization

- M/D/1: average queue length or buffer occupancy

- M/M/1: queuing delay , buffer occupancy:

- TCP:

- slow start CongWin+=1 per ACK,

- congestion avoidance CongWin+=1 per RTT,

- EstimatedRTT(k)= (1-()*EstimatedRTT(k-1) + (*SampleRTT(k), 0<(<1

- DevRTT= (1-β)*DevRTT+ β*|SampleRTT – EstimatedRTT|,  0< β <1

- TimeoutInterval = EstimatedRTT + 4*DevRTT

ATM ABR rate-based congestion control:

- Increase: Rate = min(PCR, Rate + PCR x RIF)

- Decrease: Rate = max(MCR, min[ER, Rate – Rate x RDF])

Probability distributions and stochastic processes:

- Geometric distribution: x is the number of Bernoulli experiments until success, Pr[X=k]=qk-1p, E(X)=1/p

- Binomial distribution: x is the number of successes in n Bernoulli experiments/trials , E[X]=np

- Poisson Distribution: Pr[X=k]= ((k/k!) e-(,E[X]=Var[X]= (

- Exponential distribution: f(x)=(e-(x, F[x]=1-e-(x, Pr[X>x]=1-F[x]=e-(x, E[X]=1/(