## Slide 1: CIS 4930/6930, Spring 2018 Experiment 1: Encounter Tracing using Bluetooth Due Date: Feb 19, beginning of class Ph.D. student lead: Mimonah Al-Qathrady Instructor: Ahmed Helmy
[Note: typically experiments are done in groups, usually the same groups as the project group. One report is to be submitted per group. Several groups can work together especially when more than one device is needed, but will submit different reports (and can refer to and credit one another).]
Introduction
The goal of this experiment is to gain hands-on experience in collecting Bluetooth encounter traces using classic Bluetooth and Low Energy Bluetooth.
The experiment consists of two parts: 1- simple trace collection and 2- collecting encounters scenarios between two specific devices.
Three applications are needed: a. Classic Bluetooth Scanner, b. Bluetooth Low Energy Advertiser and c. Scanner.

## Slide 2: Encounter Bluetooth Collection Application: 1) Classic Bluetooth:
This is an application for scanning other Bluetooth encounters.
The classic Bluetooth scanner will scan for other Bluetooth encounters and will save the following data into a file:
  Time of encounter
  Scanner Bluetooth MAC Address
  Scanned Device Bluetooth MAC Address
  Name of the scanned device
  Received Signal Strength Indicator (RSSI)
You do not need an advertiser to send a Bluetooth signal. Just turn on the Bluetooth Device. The Device will scan and send its Bluetooth data.
Note that the other device MAC is an actual MAC address of the other devices.
(EncountersScanner/BluetoothData.txt)

## Slide 3: 2) Bluetooth Low Energy (BLE) Applications:
There are two applications: 1- the advertiser: for sending Bluetooth Advertisement, and
2- the scanner for scanning for Bluetooth encounter.
i- Advertising Application:
Can send advertisements using transmission powers: high, medium, low, ultra-low. Advertisement include the transmission power (Tx-power), anonymous MAC address (not the actual device MAC), and the device name.
Note: assign a distinguishable name for your device Bluetooth
ii- Scanning Application:
The scanning application has a similar interface as the classic Bluetooth applications, but it scans for BLE advertisements. The scanner will record the following encountered device data:
  Time
  Encountered Device Name (Enc. Name)
  Encountered Device MAC Address (Enc. MAC)
  The transmission power of the received Advertisement( Tx power)
  The Received Signal Strength indicator (RSSI)
The information will be saved in (AScanningTXLab1/BluetoothData.txt)

## Slide 4: Manual Logging (ground truth!)
Both of the scanners has manual logging to log the time, either for the experiment or for the encounter.
For example, start experiment one:
Click number one, when you finish click one again. The data will be saved in txt file "record.txt" under the folder generated by the scanner.

## Slide 5: Part I: Bluetooth encounter trace collection
This part is to introduce you to the encounter collection for both classic Bluetooth and BLE.
Your goal is to compare and contrast the scanning result for both of them.
1. Spend some time (around 10 days) running scanners around the campus.
2. Answer the following questions:
1) How many encounters have been recorded in each scanner. (plot over time, days, hrs)
2) How many unique encounters. (plot over time)
3) What is the average number of scanned records; (how many records have been scanned per minutes in each scanner)
4) What is the max, min, mean of RSSI collected by scanners. (plot the distribution)

## Slide 6: Part II: Scanning Scenarios for Two specific devices
This part needs two devices and two users to perform the operation. (Several groups can team together if there is need for that). Also, the layout of the place needs to be known. We recommend the computer science hallway. The scenarios is described below:
Scenarios:
- 1st Scenario: Two users walking next to each other.
- 2nd Scenarios: Two users walking in different/opposite directions, but encounter for sometime.
When you start the experiment, use a manual log (‘1’ for example). Then, when you end click it again (to toggle it off). Also, when encountering in the second scenarios (use manual log to click when you encounter and when you end).
Classic Bluetooth Experiment:
The two users have to run the scanner application on each scenario. Filter the scanned data to include the other user device only.
Compare the data from each user for each scenario and plot them.

## Slide 7: Part II: Scanning Scenarios for Two specific devices (continued)
BLE Experiment:
One user runs the advertisement App, the other user will run the BLE scanner app.
Each scenario has to be run for four times. (one time for each transmission power). Each five minutes, click the advertisement button since the advertisement will stop after five minutes.
Also, filter the collected data to include only the device that sent the advertisement. (You can filter using the device name, and not the MAC address )
Compare the collected data, and plot the received RSSI on each experiment.
Questions:
-Can you deduce the scenario from the collected data? For example, by looking at the encounter data only, can you tell if the users are moving next to each other, or if the users just encounter each other, and for how long?
- How can you use the transmission power and RSSI sent in the BLE to estimate the encounters between two users?

## Slide 8: Part III: Distance Estimation from RSSI
There are several models that have been used to estimate the distance from the RSSI. In this experiment, place the devices within a specific distance from each other: 0.5m, 1m, …[X]. Plot the RSSI against the distance.
Select a model [log shadowing model, Android beacon Library, or a regression model]. Compute the Mean Absolute Error of predicted distances.

## Slide 9
Log Shadowing Model:
The popular model that describe the relationship of distance to the RSSI.
Where d=distance,
A=The average RSSI, when devices are one meter apart.
n=path loss exponent.
n=2. [free space].

## Slide 10
Android Beacons Library:
A,B and C are constants, r =RSSI, and t is the average RSSI, when devices are one meter apart.
New (Most Recent Version)-2017
Old (Previous Research)-2015

## Slide 11: Part IV: Constructing a Mobility Scenario from scanned RSSI and TX power
Assume Z, X and Y are location points. The distance between X to Z or Y should be more than M meters.
Z---------------------- X-----------------------Y
Place the Scanner on X, and use the advertiser to preform the following mobility scenarios.
Scenario 1:
Walk in normal speed from points (Z to Y), without stopping.
Scenario 2:
In this scenario, stop at X for a period of time P; Let P= M minutes. Then, move to Y]
- Run the above experiment several times using Classic Bluetooth. Then, run it using the BLE using a different TX_power setting.
- Explain how you can infer the scenarios using the RSSI.
- Is classic Bluetooth or BLE more accurate to construct the scenario? In case of BLE, which value of TX_power is more accurate for tracking purposes?

## Slide 12: Part V: Make your extension to the experiment (extra points)
Come up with other scenarios, and estimate the encounters' duration between devices.
Can you come with an algorithm that deduces the scenarios of face-to-face encounters out of Bluetooth encounter data?
Some real encounters might not be recorded by Bluetooth scanning, can you come up with an algorithm that estimates the encounters that are not reported in the Bluetooth encounter data using the data that collected by the Bluetooth device.